## Slide 1: Event plane and centrality determination
Lukáš Chlad1,2
1Nuclear Physics Institute of the CAS
2Faculty of Nuclear Sciences and Physical Engineering of the CTU

## Slide 2: Disclamer
This is not intended to give full details on the subjects, sometimes I will refer to specific articles which I think explains much better the problematics.
Mainly I am looking for your questions :)

## Slide 3: My background
Member of HADES since 2013 - TOF calibration - ECAL assembly - small data analysis of diamond START detector - participating in Low Level Data Analysis - physics analysis of kaon flow in Au+Au@1.23AGeV
Member of CBM since 2019 - Lambda simulation and data analysis with mCBM - PSD analysis -> FWALL development

## Slide 4: CONTENT
Why we need to know them?
Original PSD
Examples
Novel approach within CBM
Centrality dependence of variables, Transverse flow measurement
How the PSD handled these issues, its strengths and weaknesses
HADES Forward Wall, STAR Event Plane Detector
First ideas how to go without PSD

## Slide 5: Heavy ion Collision
Nspec = Aproj +Atarg −Npart
N produced particles ~ Npart "wounded nucleon"

## Slide 6: CENTRALITY
The centrality C is defined as the fraction of the total cross section σAA and is directly related to the impact parameter
EASY IN SIMULATION
IN REAL LIFE

## Slide 7: Why is centrality important
Many variables are highly dependent on the centrality: kinetic freeze-out temperature, multiplicity of produced particles, flow...

## Slide 8: Glauber model
Optical
From geometrical overlaps of nucleus A and nucleus B with continuum distribution of density (e.g. Woods-Saxon)
Monte-Carlo
Nucleons represented by hard spheres around center (following WS distribution) plus assumptions:
AA collisions are superposition of NN collisions
Nucleons move along straight line (even if they have collided)
Decision if two nucleons collide based on transverse distance d2 ≤ σNNinel /π

## Slide 9: How it works in SImulations

## Slide 10: How it works in REAL LIFE
Negative Binomial Distribution allow event-by-event fluctuaction
Detection efficiency (dependent on occupancy of the detector)

## Slide 11: Reaction Plane
Ideally we would like to know "reaction plane" defined by vectors of beam direction and impact parameter => again not possible experimentally
Thus different techniques were developed to overcome this lack of knowledge in real life – one of which is so-called event plane.

## Slide 12: Event plane ΨEP=Ψ1
advantages
Super easy to calculate with! Just trigonometry..
Proved technique over time (Poskanzer and Voloshin - PRC 58 (3): 1671–1678. 1998)
disadvantages
Not really good for very high multiplicities (in thousands like ALICE) => systematically underestimate the elliptic flow => cumulants are prefered (A. Bilandzic et al. - PRC 89 (6): 064904. 2014)

## Slide 13: Transverse flow
In general, we are interested where the produced particles go :) Why focus on transverse direction? With increase energy of ccollision, the longitudinal direction is uch larger and just misleads us.
"parents" of the idea Danielewicz & Odyniec (PLB 157 (2-3) 146-150. 1985)
Is studied in great details for all particle species and energies!

## Slide 14: Transverse flow
Definition
BUT there is the reaction plane which is not accessible in experiments!
Transverse => w=pT
The imprecision coming from using EP instead of RP leads to correction:
It is important to also disentangle the direction of flow of particles we are interested in and those which we use for EP determination!

## Slide 15: EP resolution correction
Method by Jean-Yves Ollitrault [arxiv:nucl-ex/9711003]
Analytically can be derived:
From "2-subset" technique (random division of detections into 2 subsets)
Leads to:
STAR: 10.1103/PhysRevC.93.014907

## Slide 16: Projectile spectator detector
"The main purpose of the PSD is to provide an experimental measurement of a heavy-ion
collision centrality and orientation of its symmetry plane. Precise event-by-event estimate of these basic
observables is crucial for many physics phenomena studies to be performed by the CBM Collaboration.
The PSD is a compensating lead-scintillator calorimeter* designed to measure the energy distribution
of the projectile nuclei fragments (spectators) and forward going particles produced close to the beam
rapidity. "
*compensating means the same respons to electromagnetic and hadronic shower, using the sandwich Pb/Scint ratio 4:1

## Slide 17: Design
Design Requirements
Spectators detection in the beam energy range of Eb = 2 − 35 AGeV.
Operation at beam intensities up to 109 Au ions per sec.
Reaction plane determination with an accuracy better than 40 degree.
Determination of collision centrality classes with an accuracy better than 10%.
How to fullfill them?
Large area ~ 1.5x1.5 m2
σE/E < 60%/sqrt(E[GeV])
Granularity 20x20 cm2 (4 times smaller module size did not have significant improvement on EP resolution)
Radiation hard photon detector with high-rate capability (Micro-Pixel Avalanche Photodiod)
60 Pb+Scint pairs divided into 10 individually read-out sections
~ 6 interaction lengths
44 modules

## Slide 18: Performance in sim
Centrality determination
Event plane resolution

## Slide 19: Performance @ NA61
Energy resolution
centrality
Event plane resolution
https://doi.org/10.22323/1.347.0195
https://doi.org/10.1016/j.nuclphysa.2018.10.058

## Slide 20: HADES FORWARD WALL
Located 7m downstream from the target region (polar angle between 0.33° and 7.17°)​
Linear dependence of signal amplitude ​on fragment charge

## Slide 21: Design
Scintillator hodoscope (depth ~2.5 cm) 140 small cells (4x4 cm2)
64 middle cells (8x8 cm2)
84 large cells (16x16 cm2)
Instruments and Experimental Techniques 57 (2): 103-119. 2014

## Slide 22: Performance
Time resolution
Freagment charge identification

## Slide 23: Event plane determination
Effects of non-uniform acceptance / tilt of beam PRC 77 (2008) 034904

## Slide 24: Centrality determination
Usually, HADES is using Nhit as a variable defining the centrality classes
But in case of (net)proton number fluctuation one needs to avoid as much autocorrelations as possible.
It is to define centrality classes in terms of bins of summed charges in FWall.
https://doi.org/10.1103/PhysRevC.102.024914

## Slide 25: Event plane detector @ STAR
Replaced original BBC in 2017 (within STAR forward physics upgrade)
Measures charged particles emitted in the forward and backward directions, at angles 0.7◦ < θ < 13.5◦
https://doi.org/10.1016/j.nima.2020.163970

## Slide 26: Design
Replacement of original BBC
Beam to Beam Counter used for multiplicity measurement (was used for triggering purposes)
In principle could be as well used to determine EP but with quite bad resolution
Inner structure
Of EPD
12 supermodules (1 is highlighted in figure) covering 30 deg. divided into 31 cells, disk radius 0.9m, hole of 4.6cm
1.2cm thick plastic scintillator read-out with wavelength shifter and optical fiber which that guides the light to SiPM

## Slide 27: Performance and new physics
Resolution
Allowed to study
Global lambda polarisation
Significantly improved flow measurement (EP resolution)
Fluctuation studies (independent centrality determination plus increased phase space coverage)
(18.6 cm) / sqrt(2)c ≈ 0.44 ns

## Slide 28: Forward Wall @ CBM ?
First shots in simulations
Idea: combine FWALL of HADES (scintillator tilts)
EPD of STAR read-out with WLS and SiPM
CBM hadron setup with replaced PSD by FWALL

## Slide 29: Design and transport results
FWall design
FWALL size is 160 cm x 128 cm x 10 cm FWALL contains 220 modules One quadrant: Number of SMALL modules: 6 x 4 – 4 (hole) Number of MEDIUM modules: 3 x 2 Number of LARGE modules: 2 x 2 Small: 4x4 cm2 Medium: 8x8 cm2 Large: 16x16 cm2
Modules back side (red is air channel, gold is WLS fiber)
FWall points XY distribution
after running UrQMD Au+Au @ 6AGeV

## Slide 30: SUMMARY
Introduction into centrality and event plane determination
Examples of working detectors at other experiment
First look at simulations for new FWALL

## Slide 31: THANK YOU for your attention !!