## Slide 1
PRR of the PSD MPPCs and readout electronics
Fedor Guber, Dmitry Finogeev, Nikolay Karpushkin,
Alexander Makhnev, Sergey Morozov,
Dmitry Serebryakov
INR, Moscow
on behalf of the PSD team
:
INR, Moscow Russia;
MEPHI, Moscow, Russia;
NPI, Řež, Czech;
CTU, Prague Czech;
GSI, Darmstadt, Germany;
TU, Darmstadt, Germany;
PSD

## Slide 2
PSD readiness:
All 46 PSD modules have been constructed;
PSD modules response has been studied on cosmic muons and test beams at CERN.
Upper part of the support structure is ready. Lower part is under development.
At present, part of modules is used at BM@N and NA61/SHINE experiments in the framework of FAIR–phase -0.
One module (mPSD) is used at mCBM.
Projectile Spectator Detector (PSD)
PSD - sampling lead/scintillator forward hadron calorimeter with beam hole in the center.
PSD – modular structure: 46 modules 20x20x165 cm3.
Total weight – 23 tons.
PSD will be placed at distance ~10.5 from the the target.
  PSD configuration
for Day-1 CBM experiment
The main purpose of the PSD is the measurement
of centrality and orientation of reaction plane
in heavy ion collisions at interaction rate up to 106 per sec.
2

## Slide 3
Structure of the PSD modules
PSD module:
60 Pb/scint. samples. (Pb (16mm) + Scint (4mm) )
Longitudinal segmentation:
light collections – 6 WLS fibers from 6 sequentially scint. tiles
are combined into one optical connector at the end of module.
Photodetectors: 10 MPPC (3x3 mm2) per module
Length of the module – 5.6 λint
Weight – 500 kg
MPPC Hamamatsu S14160-3010P
Sensitive area - 3 x 3 mm2
Number of pixels - 90 000
nominal gain - 1 x 105,
Gain temperature stability ~1% /1ᵒC
Pixel recovery time - 10 ns
PDE -18%
.
See S.Morozov presentation
3
PSD module scintillators assembly
Scintillator tiles
WLS fibers
Lead
Notes: 3

## Slide 4
PSD readout electronics
Radiation sensitive electronics will be placed at the distance ~ 50m from the PSD in radiation protected area:
ECAL@PANDA ADC64 board (LTM9011 ADC 125Msps / 80Msps (14-bit digitization; 2VP-P) with ADC interface board (single-ended to differential converter)
Board with 10 MPPCs,
a temperature sensor
and LED for calibration
are mounted on rear side of modules
Remotely controlled MPPC bias voltage supply.
LED pulse generator
AuAu@11 AGeV
Beam rate – 108 Au/s
1% Au target
Neq/cm2 after 1 month
5
See A.Makhnev and D.Finogeev presentation.

## Slide 5
Full chain of mPSD readout has been successfully integrated
in mCBM readout and tested at high interaction rate.
Time correlation with other subsystems
mPSD energy spectra are in agreement with simulated mPSD data
Full PSD readout chain test in at mCBM
Run 1588 O+Ni 2.0AGeV,
0.7MHz interaction rate
Taken 15.07.2021
Experiment & Simulation
6
See D.Finogeev and N.Karpushkin presentation.

## Slide 6
The PSD supermodule performance
PSD СВМ supermodule
on T9/T10/NA61/SHINE test beams
at CERN
Energy resolution and linearity response
N Karpushkin, D Finogeev, M Golubeva, F Guber, A Ivashkin,
A Izvestnyy and S Morozov
J.Phys.Conf.Ser. 1667 (2020) 1, 012020
4

## Slide 7
Plan of PRR of PSD MPPCs and readout electronics presentations
Sergey Morozov - PRR of PSD MPPCs.
Alexander Makhnev – PRR of FEE and readout electronics (I):
Status of PSD electronics development and tests.
Readiness to mass production.
Dmitry Finogeev - PRR of FEE and readout electronics (II):
Integration and test of the full PSD readout chain at the mCBM.
Nikolay Karpushkin - PSD signals processing and calibration.
mPSD beam test results at mCBM.
Method of pile-up recovery/rejections.
7

## Slide 8
Thanks for your attention