## Slide 1: PRR of FEE and readout electronics (II): The full PSD readout chain integration and test at the mCBM
D.Finogeev, INR, Moscow
on behalf of the PSD team

## Slide 2
Outline
PSD FEE and readout
  ADC board for ECAL@PANDA
  ADC board integration to mCBM with GBT
  CRI PSD firmware unit
  Baseline drift
  FIR filter FPGA resources estimation
  Conclusion

## Slide 3: Full PSD readout chain setup at mCBM
PSD module was integrated into mCBM with full chain PSD readout:
  ADC + interface boards
  MPPC board
  60m coaxial cable
MPPC board mounted on PSD module @mCBM
ADC64 FPGA board + interface board installed in DAQ container and connected with 60m coaxial cable to PSD module @mCBM
Results are published in:
“Development of readout chain for CBM Projectile Spectator Detector at FAIR”
DOI: 10.1088/1742-6596/1690/1/012059

## Slide 4: ADC board at mCBM 2021
  ADC board was designed for ECAL@PANDA
  LTM9011 ADC;
    125Msps / 80Msps (used now); 14-bit digitization; Selectable Input Ranges: 1VP-P to 2VP-P (used);
  Two FPGA Kintex 7
    32 channels per one FPGA; Separated optical link for each
  Readout rate
    3.2 (4.8) Gb/s; 16.5 GBT words per event (32 channels fired)
    Max hit data size (2MHz hit rate): ~40 bit
ADC64 FPGA board + interface board @mCBM May 2021

## Slide 5
PSD readout integration into mCBM DAQ
GBT FPGA is used for the connection to CRI board
CRI clock is used for the ADC board
  Internal clock used to synchronize GBT
  After GBT starts provide recovered clock from CRI, the clock MUX switched GBT Rx clock
  Time stamp provided by CRI via GBT
The ADC boards assembly is controlled via GBT
  The ADC FPGA is connected via I2C to MCU on the ADC interface board
Results are published in:
“The readout system of the CBM Projectile Spectator Detector at FAIR”
DOI: 10.1088/1748-0221/15/09/C09015
ADC – CRI clock, data, control overview scheme

## Slide 6
PSD ADC firmware development and INR RAS, Moscow
ADC firmware features:
Analog signals acquisition individually for each channel by threshold crossing
Force triggered acquisition s is possible by ‘and’ and ‘or’ combinations of channels events and asynchronous pulser
Online monitoring of the baseline zero level and the noise RMS, measuring readout rate in range 0.5 to 4.5MHz.
GBT tested with KC7 evaluation bard (at INR RAS, Moscow) and CRI (GBI, Darmstadt)
KC7 evaluation board
ADC board
PSD readout setup at INR RAS, Moscow
Readout software interface (IP-bus, C)

## Slide 7
The PSD-CRI unit used for beam tests in June 2021
The Prototyped with KC7 evaluation board in January 2021
Crucial modules:
  ADC control (GBT slow control)
  Data reader (read GBT data from ADC)
  Data sorter (combine data from (1-8) ADCs into one buffer, dataflow throttling)
  FLIM interface (push data to FLIM)
8 GBT links, 4 FLIM interfaces per SLR
PSD-CRI firmware specific unit design for test at mCBM June 2021

## Slide 8
The Data sorter will be excluded as excess element
Single GBT link per FLIM interface
Max FLIM interface load 64+16 bit @40MHz through async FIFO
8 ADC boards, 16 GBT links in total for PSD
8 FLIM interfaced / 8 GBT links per SLR
PSD GBT spare solution is use wide bus mode:
  120bit @40MHz = 4,8Gb/s per FLIM interface
  38,4 Gb/s per SLR
  76,8 Gb/s per CRI
No start/stop is required (always ready)
No huge buffering data
Input throughput = output throughput
FLIM throughput:
PCIe 6-7GB/s
50 Gb/s per SLR
100 Gb/s per CRI
PSD-CRI firmware specific unit revision

## Slide 9
ADC baseline drift while high load
ADC baseline drift during high rate because of capacitance in FEE input filter
  The firmware exponential filter compensation was prepared for beam tests.
  Correction allowed to measure signal charge with base line drift during the beam test.
  Because of tuned threshold ~ 0.8 MIP (1,4mV) compensation accuracy was not enough to avoid continuous triggering during base line drift.
  Data processing will be based on FIR filter

## Slide 10
Emulation of signal FIR filter placement in FPGA KC7
11 DSP modules was implemented in ADC firmware design to check FPGA resources availability for FIR signal processing
A(i)*c1+A(i-1)*c2+...+A(i-10)*c11
11 x DSP: A(14 bit) * B (14bit) + C(28 bit) = P(29bit) @80MHz
DSPi: adc(i) * const(i) + dsp_out(i-1)(27 downto 0)
ADC FPGA utilization
beam tests mCBM@2021 design + FIR emulation
DSP placement in firmware design

## Slide 11
PSD full readout chain was tested at beam tests with common mCBM DAQ in June 2021
FEE + 60m signal cable + ADC boards assembly
GBT connection stability
ADC signal digitizer firmware
CRI data processing firmware
ADC control + slow readout (python macro)
Event time synchronization
Issue was observed: ADC baseline drift during high rate because
  Firmware exponential filter compensation was implemented for charge correction
  Solution 2: Working on signal FIR processing FPGA with self-channel triggering without threshold-crossing procedure
One FPGA on board was used during the tests
80 MHz ADC clock used, 120 MHz clock is not ready